## Slide 1
WHAT PREDICTS NEXT-VISIT CARDIOTOXICITY?
NON-CNN FEATURE ANALYSIS
15% MID-GLS DECLINE
Notes: A concise presentation of the non-CNN feature-importance analysis.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
[/Sources]

## Slide 2
2
One-visit-ahead prediction, defined consistently
patients
events 49 vs 189 non-events
current → next visit predictions
103
238
20.6%
TASK
At each eligible visit, use only information already available to predict whether the immediately following visit shows ≥15% relative Mid-GLS decline from the first-visit baseline.
Notes: The unit is a current-to-next-visit transition, and all transitions from a patient stay in the same held-out fold.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
[/Sources]

## Slide 3
3
The three feature families capture different information
Current and first-visit GLS/EF plus relative changes and slopes
Dispersion across segments in peaks, timing, and curve behavior
Matched-layer amplitude, timing, correlation, and curve-shape gaps
CLINICAL
ENDO–MID
VARIABILITY
FEATURE FAMILIES
Clinical features summarize global function and trajectory. Endo–Mid features compare matched layer curves. Variability features measure disagreement among myocardial segments.
Notes: Clinical example: first_endo_gls is the absolute first-visit Endocardial GLS magnitude. Endo–Mid example: d_tm_sd_gap_dct04 compares paired layer curves, summarizes segmental gap variability over time, applies DCT04, and takes current minus previous visit. Variability example: circular dispersion of Endocardial segment time-to-peak.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_next_visit_gpu_results/feature_manifest.csv
[/Sources]

## Slide 4
4
Non-CNN model performance
BEST AP
0.313 Combined Extra Trees
BEST AUC
0.672 Combined Extra Trees
REFERENCE
Random: AUC 0.500 Expected AP 0.206
Chart: 
| Clinical | + Endo–Mid | + Variability | Extra Trees
AUC ×100 | 63.1 | 64.4 | 65 | 67.2
AP ×100 | 28.9 | 30.9 | 28.8 | 31.3
Notes: AUC improved from 0.631 for the clinical ridge to 0.672 for Combined Extra Trees. AP improved from 0.289 to 0.313; the event-rate reference is 0.206.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_base_metric_reproduction.csv
[/Sources]

## Slide 5
5
Feature contribution was tested on held-out patients
1 FIT
2 SHUFFLE
3 MEASURE
Break one feature
Randomly permute that feature in held-out patients while leaving all others unchanged.
Train by patient
Three repeated five-fold splits; every visit from one patient stays together.
Observe the loss
The decrease in AUC or AP is its predictive contribution. Patient bootstrap gives 95% CIs.
Notes: Permutation importance asks whether held-out prediction gets worse when one feature is made uninformative. Positive drops indicate genuine model dependence.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
[/Sources]

## Slide 6
d_tm_sd_gap_dct04
1. Pair Endocardial and Mid-wall curves from each matched segment.
2. At every cardiac-cycle point, compute Endo − Mid for each segment.
3. Across segments, calculate the SD of that gap, producing an SD-gap curve.
6
Top sparse-model feature: changing Endo–Mid heterogeneity
4. Apply the Discrete Cosine Transform and keep DCT04, a phase-dependent pattern component.
5. Subtract the previous visit: current DCT04 − previous DCT04.
Meaning: the timing pattern of layer-to-layer disagreement across segments changed—not simply that variability became larger. ΔAUC 0.037 (95% CI 0.001–0.066); ΔAP 0.043.
Clinical
Endo–Mid
Variability
Notes: This is the strongest engineered feature in the sparse Endo–Mid model. DCT04 describes a mid-frequency temporal pattern rather than a single time point.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
[/Sources]

## Slide 7
cur_tm_mean_shape_gap_dct01
1. Normalize each Endocardial curve by its own maximum absolute amplitude.
2. Normalize the matched Mid-wall curve the same way.
3. Compute normalized Endo − Mid at each time point and average across segments.
7
Top Extra Trees feature: normalized layer separation
4. Apply the DCT and keep DCT01—the broad average level of the shape-gap curve.
Because amplitude is normalized first, the feature emphasizes shape differences more than strain magnitude.
Meaning: systematic separation between Endocardial and Mid-wall contraction patterns at the current visit. Extra Trees uses nonlinear thresholds, so there is no single global risk direction. ΔAUC 0.017 (95% CI 0.008–0.026); ΔAP 0.020.
Clinical
Endo–Mid
Variability
Notes: DCT01 summarizes broad curve separation after per-curve normalization. This was the most important feature within Combined Extra Trees.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
[/Sources]

## Slide 8
CLINICAL • first_endo_gls
Absolute magnitude of first-visit Endocardial GLS: |baseline Endo-GLS|.
Example: −21.4% becomes 21.4% and is carried forward for that patient.
ΔAUC 0.018 (95% CI 0.003–0.035). Its direction may reflect reserve, correlation, or regression to the mean—not causality.
8
Clinical GLS was useful; segment variability was weaker
VARIABILITY • Endo time-to-peak dispersion
For each Endocardial segment, obtain normalized time-to-peak. Because cardiac time is cyclic, summarize their spread with circular SD.
Meaning: how synchronized—or dispersed—the segments are in reaching peak strain. ΔAUC 0.008 (95% CI 0.003–0.014); ΔAP 0.007. Positive but smaller than the leading Endo–Mid signals.
Clinical
Endo–Mid
Variability
Notes: Baseline Endocardial GLS was the strongest stable clinical feature. The most stable variability feature measured circular dispersion of segmental time-to-peak.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
[/Sources]

## Slide 9
9
Six features had stable positive held-out AUC importance
RANKING
ΔAUC is the performance lost after shuffling the feature. Only patient-bootstrap intervals entirely above zero are shown.
Plain-language feature | Family | Model | ΔAUC | 95% CI
Change in phase pattern of segmental layer-gap variability | Endo–Mid | Clinical + Endo–Mid | 0.037 | 0.001–0.066
Baseline Endocardial GLS magnitude | Clinical | Clinical ridge | 0.018 | 0.003–0.035
Overall normalized Endo–Mid shape separation | Endo–Mid | Extra Trees | 0.017 | 0.008–0.026
Finer temporal pattern of normalized shape separation | Endo–Mid | Extra Trees | 0.009 | 0.002–0.015
Endocardial segment time-to-peak dispersion | Variability | Extra Trees | 0.008 | 0.003–0.014
Change in mean vendor Endo–Mid peak gap | Endo–Mid | Extra Trees | 0.005 | 0.001–0.010
Notes: The stable list is dominated by Endo–Mid features. Baseline Endocardial GLS and one segment-timing dispersion feature also remained stable.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
[/Sources]

## Slide 10
10
At family level, Endo–Mid carried the clearest signal
Clinical ΔAUC
Variability ΔAUC
Endo–Mid ΔAUC
−0.008
+0.054
+0.016
COMBINED EXTRA TREES • FAMILY PERMUTATION
All features from one family were shuffled together. This captures contribution even when correlated features can substitute for one another.
Notes: In Combined Extra Trees, grouped shuffling caused the largest AUC loss for Endo–Mid features. Clinical features were redundant in this nonlinear combined model.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_family_importance.csv
[/Sources]

## Slide 11
11
Bottom line
First-visit baseline One-visit-ahead target
Interpret DCT cautiously Validate externally
Prioritize Endo–Mid shape + change
1
2
3
TAKE-HOME
The results support the Endo–Mid hypothesis more strongly than the inter-segment variability hypothesis, but the gain over clinical prediction remains modest.
Notes: The deck is deliberately concise. The detailed Markdown report contains the full feature descriptions, model-specific rankings, and interpretation cautions.
[Sources]
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_report.md
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_importance_top.csv
- D:/us/cardiotoxicity_feature_importance_results/noncnn_feature_family_importance.csv
[/Sources]